Input Modes Quick Start
- a.) Momentary: when a Button is pressed, the corresponding Relay is closed, when the Button is released, the Relay opens.
- b.) Toggle: when a Button is pressed the Relay closes, when a Button is pressed again, Relay opens.
- c.) Interlock: Only one of the group outputs are active at any one time; if both Inputs are present, no output is on.
- d.) Pri. Interlock: (Priority interlock) Only one of the group outputs are active at any one time, if a second Input becomes active, the output which is already active has priority and stays on.
- e.) 1on1off: Button 1 of the group turns the Relay on, Button 2 of the group turns the Relay off.
- f.) 2on2off: Button one and two pressed together turns on Relay 1 and Relay 2; Button one and two pressed together again turns the Relay off.
- g.) On Timed Off: The Buttons turn the corresponding Relay on, and after a set amount of time, the Relay automatically turns off. The delay time can be specified below, individually on a per Group basis.
- h.) On Hold Timed Off: The Button turns the corresponding Relay on, and on Button release, the hold timer starts, which holds the Relay for a specified amount of time. after which, the Relay automatically turns off.
- i.) Timed ON: When a button is pressed, a timer starts. When the timer is expired, the corresponding Relay will close.
- j.) Hold Timed On: Button is pressed, and then, when released a timer starts. After the timer is expired, the corresponding Relay will close.
- k.) Local relay: The unit does not transmit any signals, rather, the corresponding relay on board will be operated.
- l.) Disabled: The corresponding group's Relays will never activate